## Slide 1: ICMS DEGREE COLLEGE
BCS 5th
Network Strategies
Malik Zahoor Khan MS Computer Networking.

## Slide 2: Circuit Switching
Create a direct physical connection b/w two devices such as phone or Computers.
Example
Instead of point to point connections b/w the three telephones on the left ( A, B, and C) to the four telephones on the right (D,E,F and G) requiring 12 links. we can use four switches to reduce the number and the total length of the links.
Telephone A is connected through switches I ,II and III to telephone D.
By moving the levers of the switches, any telephone on the left can be connected to any telephone on the right

## Slide 3: Circuit Switching
A circuit switch is a device with n input and m output that create a temporary connection b/w an input link and an output link.

## Slide 4: Two types of Circuit Switching
1. Space Division Switch
2. Time division Switch

## Slide 5: Space Division Switch
In space division switching the paths in the circuit are separated from each other spatially
This technology was originally designed for use in Analog networks but is used currently in both analog and digital network.
1. Crossbar switch
2. Multistage switch
3. multiple Paths
4. Blocking.

## Slide 6: Crossbar Switching
It connects n inputs to m outputs in a grid using electronic micro switches (transistors) at each cross point.
Example
Connecting n inputs to m outputs using a cross bare switch requires n x m cross points.
To connects 1000 input and 1000 outputs requires a crossbar with 1,000,000 cross points.
A cross bare with this number of cross points is impractical.

## Slide 7: 2.Multistage switch
The solution to the limitations of the crossbar switch is the multistage switch,
Which combines crossbare switches in several stages.
Multistage switching devices are linked to switch that, in turn, are linked to other switches.
For example
Imagine that we want a multistage switches to do the of a single 15 by 15 crossbar switch.
Assume that we have decided on a three stage design that uses three switches in the first and final stages and two switches in the middle stage.
There are (5 x 3=15)

## Slide 8: 3. Multiple paths.
Multistage switches provide several options fir connecting each pair of linked devices.
Let us compare the number of cross points in a 15 by 15 single stage cross bare switch with the 15 by 15 multistage switch.
In the single stage switch we need 225 cross points (15x15)

## Slide 9: Multistage switch need
1. three first stage switch. Each with 10 cross points (5x2) for total of 30 cross points at the first stage.
2. two second stage switches each with 10 cross points (3x3) for a total of 18 cross points at the second stage.
3. three third stage switches, each with 10 cross points (5x2) for a total of 30 cross points at the last stage.
The total numbers of crosspoints required by our multistage switch is 78.

## Slide 10: 4. Blocking
This savings comes at a cost.
The reduction in the number of crosspoints results in a phenomenon called blocking during period of heavy traffic.
Blocking refers to times when one input cannot be connected to an output because there is no path available b/w them.

## Slide 11: 2. Time- Division Switch
Time – division switching uses time division multiplexing to achieve switching.
Two popular methods used in time division multiplexing.
1. Time – Slot Interchanges (TSI)
2. TDM Bus.

## Slide 12: Time slot Interchange
A system connecting four input lines to four output lines.
Imagine that each input line wants to send data to an output line according to the following pattern
1 3 2 4 3 1 4 2

## Slide 13: TSI
The TSI works in RAM with the several memory locations.
The size of each location is the same as the size of a single time slot.

## Slide 14: TDM Bus
It is very simplified version of a TDM Bus.
The input and output lines are connected to a high speed bus through input and output gates (Microswitches)
Each input gate is closed during one of the four time slots.
During the same time slot only one output gate is also closed
This pair of gates allows a burst of data to be transferred from one specific input line to one specific output line using the bus,
The control unit opens and closes the gates according to switching need.

## Slide 15: Example
The first time slot input gate 1 and output gate 3 will be closed during the second time slot ,
Input gate 2 and output gate 4 will be closed and so on.

## Slide 16: Space and Time division Switch combination
When compare space division and time division switching, some interesting facts emerge,
The advantage of space division switching is that it is instantaneous.
The disadvantage is the number of crosspoints required to make space division switching acceptable in terms of blocking.
The advantage of time division switching is that
It needs no crosspoints.
And the disadvantage in the case of TSI is that processing each connection creates delays.
Each time slot must be stored by the RAM then retrieved and passed on.

## Slide 17: Frame Relay
Frame relay is a virtual circuit wide area network that was designed to respond to demands for a new type of WAN in the late 1980s and early 1990s.
Prior to Frame Relay, some organizations were using a virtual circuit switching network called X.25 that performed switching at the network layer.
Example
The internet which needs wide area networks to carry its packets from one place to another used X.25.
X.25 is still being used by the internet, but it is being replaced by other WANs.

## Slide 18: X.25 Drawbacks
1. X.25 has a low 64kbps data rate , by the 1990 there was a need for higher data rate WANs.
2. X.25 has extensive flow and error control at both the data link layer and the network layer.
This was so because X.25 was designed in 1970.
When the available transmission media were more prone (Downwards) to errors.
Flow and error control at both layers create a large overhead and slow down transmission.
X.25 requires acknowledgments for both data link layer frames and Network layer packets that are sent b/w nodes and b/w source and destination.

## Slide 19: X.25 Drowbacks
3. X.25 was designed for private use, not for the internet.
X.25 has it own network layer.
This mean that the users data are encapsulated in the network layer packets of X.25.
The internet has own network layer which mean if the internet wants to use X.25, the internet most deliver its network layer packet, called a datagram, to X.25 for encapsulation in the X.25 packet.

## Slide 20: Frame Relay
FRAME RELAY operates at a higher speed (1.544Mbps and recently 44.376Mbps).
FRAME RELAY operates in just the physical and data link layers.
FRAME RELAY allows busty data
It allows frame size of 9000bytes,which can accommodate all local area network frame sizes.
It is less expensive than other traditional WANs.
It has error detection at the data link layer only.

## Slide 21: ATM
Asynchronous Transfer Mode is the cell relay protocol designed by the ATM Forum and adopted by the ITU-T.
It is high speed interconnection of all the worlds networks.
It is a highway for information highway.

## Slide 22: Design Goals ATM
Foremost is the need for a transmission system to optimize the use of high data rate transmission media in particular optical fiber.
The system most interface with existing system and provide wide area interconnectivity b/w them without lowering their effectiveness or requiring their replacement.
The design must be implemented inexpensively so that cost would not be a barrier to adoption. if the ATM become the backbones of international communications, as intended, it must be available at low cost to every user who wants it.

## Slide 23: Design goals
The new system must be able to work with and support the existing telecommunications hierarchies (local loops, local providers, long distance carriers, and so on)
The new system must be connection- oriented to ensure accurate and predictable delivery.
Last but not least, one objective is to move as many of the functions to h/w as possible (for speed) and eliminate as many s/w functions as possible (again for speed)